Paper Number: MC03-201

An ASAE Meeting Presentation

Drift Characteristics of Spray Tips Measured in a Wind Tunnel

Robert E. Wolf, Assistant Professor

Bio and Agricultural Engineering Department

Kansas State University, 229 Seaton Hall

Manhattan, KS 66506

email: rewolf@ksu.edu

Written for presentation at the

2003 Mid-Central Conference of ASAE

Sponsored by ASAE

Ramada Inn

St. Joseph, MO

April 4-5, 2003

Abstract.   A wind tunnel, water-sensitive papers (wsp), and DropletScan( software were used to collect and compare the movement of spray droplets downwind  from different types of ground sprayer tips.  The wind tunnel was equipped with a plant canopy and a single nozzle boom to simulate a field application.  A constant wind speed of 4.6 m/s was used for the test.  Twenty-two nozzle types were individually tested with a perpendicular orientation to the wind direction.  Each nozzle was tested at a flow rate of 1.5 liters per minute and a pressure of 276 kPa.  Water-sensitive papers were placed at canopy height 1, 2, and 3 meters downwind to collect the spray droplets escaping the spray swath.  Percent area coverage for each wsp was generated by DropletScan( for comparative purposes.  High amounts of coverage would support an increased potential for spray drift..  Many differences were found among all nozzle types at all locations.  At the 1-meter location, the amount of coverage ranged from a high of 98.7 percent with a traditional flat-fan design to a low coverage of 8.4percent with the chamber design turf flood.  The venturi style nozzles as a group performed best overall with coverages ranging from 35.7-9.4 percent.  The group mean for the venturi nozzles was 20.2 percent.  This is compared to the flat-fan group at 90.4 percent, the preorifice and chamber styles at 42 percent, and the hollow cones at 72.3 percent.  With a few exceptions, similar trends were found at the 2 and 3 meters locations.  This study supports the use of drift reducing nozzles as a means for minimizing the potential for spray drift.  Some are better than others.

Keywords.  Spray drift, Spray tips, DropletScan(, Droplet size, Wind tunnel, water sensitive paper

Introduction

Controlling or minimizing the off-target movement of sprayed crop protection products is critical.

Researchers have conducted numerous studies over time to better understand spray drift problems.  Particularly, a recent group of studies conducted by the industries Spray Drift Task Force (SDTF, 1997) generated numerous reports to support an Environmental Protection Agency (EPA) spray drift data requirement for product reregistration and future label guidance statements on drift minimization.

Even though a better understanding of the variables associated with spray drift exists, it is still a challenging and complex research topic.  Environmental variables, equipment design issues, many other application parameters, and all their interactions make it difficult to completely understand drift related issues (Smith, et al., 2000).  Droplet size and spectrum has been identified as the one variable that most affects drift (SDTF, 1997).  Many forces impinge on droplet size, but it is still the drop size that must be manipulated to optimize performance and eliminate associated undesirable results (Williams, et al., 1999).  Drift is associated with the development of high amount of fine droplets (Gobel and Pearson, 1993).  Wolf, et al., (1999, 2000, 2001, 2001) in field studies, found that commonly used flat spray nozzle types exhibited significantly different potential to drift.

Over the last several years there has been an increased interest by nozzle manufactures to design nozzles that will effectively reduce the volume of driftable fines found in spray droplet spectrums.  This is being successfully accomplished with the use of a preorifice and also with turbulation chambers (R. Wolf, 2000).  A recent trend with spray nozzle design is to incorporate a ‘venturi’ that includes the spray droplet in air to lessen the drift potential while still maintaining adequate efficacy.  Several nozzle manufacturers are including this new design as a part of a marketing campaign for drift control.  Early research would indicate that the venturi nozzle is producing larger spray droplets (Womac, et al., 1997; Ozkan and Derksen, 1998; R. Wolf, et al., 1999, 2001, 2001).

Spray drift data collection in the field is very complicated, expensive, and time consuming.  Efforts and techniques to use wind tunnels to measure spray drift from various boom sprayer nozzle types are being developed (Phillips and Miller, 1999).  Wind tunnel studies with simple nozzle mounting structures can provide valuable nozzle performance data independent of a sprayer and tractor while reducing much of the variability experienced in the field measurement process (Miller, 1993).  Phillips and Miller (1999) determined that wind tunnel experiments are adequate to simulate the results of field measurements for spray drift.

# Objective

The objective of this study was to compare in a wind tunnel the amount of downwind spray droplet movement (drift) from several different agricultural spray nozzles.

# Procedure

This study was designed to measure and compare in a wind tunnel the amount of downwind spray droplet movement (drift) from 22 different nozzle designs (table 1).  All nozzles were compared at a flow rate of 1.5 liters per minute (0.4 gpm).  The spray pressure was maintained at 276 kPa (40 psi) for all treatments.

Applications using water with a single nozzle boom configured for use in a wind tunnel were made at a constant wind speed of 4.6 m/s (10.3 mph) throughout the experiment.  Each nozzle treatment was positioned perpendicular to the wind direction.  The nozzles were located from 45.7 to 50.8 cm (18-20 inches) above the canopy.  A canopy, 25 cm (10 inches) high, was placed on the wind tunnel floor to simulate field conditions for a postemergence spray application. The canopy consisted of plastic broadleaf plants that were placed randomly through the entire length and width of the tunnel.  Simulated grass was placed on the floor of the tunnel under the boom to minimize spray droplet bounce.

Water sensitive papers (Syngetna, 2002), were placed at canopy height downwind from the spray boom to function as collectors for the droplets moving away from the spray swath.  Three water sensitive papers (wsp) were located at 1, 2, and 3 meters downwind over four replications for each treatment.  A flatbed scanner (HP 6200Cse, 1200 pixels, Hewlett Packard, Palo Alto, CA), a computer, and DropletScan( software (WRK of Arkansas and Oklahoma, Devore Systems, Inc, Manhattan, KS) were used to capture the droplet images and generate the droplet information.  Tests for equality of means were performed using PROC GLM.  The nozzles were placed into four groups based on design and pattern for further statistical analysis (table 1).  The groups compared were: traditional flat-fan, preorifice and chamber flat-fan, hollow-cone, and venturi flat-fan.

A boom with pressure gauge was designed to position one nozzle per treatment in the wind tunnel 14 meters (47 feet) downwind from the beginning of the working section of the wind tunnel.  A QJC364 nozzle body (Spraying Systems Co., Wheaton, IL) with a pulse width modulation (PWM) valve (Capstan Ag Systems, Inc., Topeka, KS) attached to the diaphragm check valve was used for connecting and controlling each nozzle.  The collector was designed for removal from the wind tunnel after each treatment to facilitate wsp removal and replacement with dry, clean wsp for the next treatment.

Nozzles and wsp were placed in position for each treatment by the researcher and assistants.  The PWM valve was connected to a timer and used to control the length of spray cycle.  The PWM valve allowed the system to be preset to the treatment pressure for instant and accurate spray volume control.  In this study it was determined that a 2-second spray interval was needed to achieve adequate coverage to analyze the droplets on the water sensitive paper.  All controls were actuated from a control room outside the wind tunnel.  The wall was equipped with a door to facilitate nozzle changing and a viewing window to verify the equipment functioned properly.

The wind tunnel used in this study had a working section 17m long, 1.5m wide, and 1.9m high (58 x 5 x 6.5ft.).  A recirculating push-type fan (tip to tip blade measurement, 2.0 m, 6.5 ft.) driven by a 125 HP General Electric DC motor was used to develop the air stream.  A diffuser the size of the wind tunnel cross-section was placed at the start of the working end of the tunnel.  The diffuser was made from steel pipe (5.1 cm in circumference by 30.5 cm long) welded to form a honeycomb design.  Spires, designed to increase both the depth and turbulence level of the wind tunnel boundary layer, were placed at the base of the diffuser.

Temperature and humidity were measured using a Campbell Scientific CR10X probe system with data logger.  The probes were positioned at boom height.  A KURZ Model 1440M air velocity meter positioned above and near the center of the boom was used to continually monitor wind velocity.  Wind velocity was controlled by adjusting the amperage to the fan motor.

Results and Discussion

Water-sensitive papers (wsp) are often used as an indicator for the presence of spray deposition (Matthews, 1992).  Water in the spray stains the wsp and the spot size can be observed or measured, thus, permitting the use of wsp to evaluate the number of droplets per unit area and for measuring the percent area covered (Syngenta, 2002).  Spray droplets moving downwind and collected on water sensitive paper are a good indicator of a spray tips potential for drift when measuring the amount of coverage obtained on the cards (Wolf, 1999).  One statistic generated by DropletScan( software is percent area coverage.  Since the wsp are placed outside and downwind from each treatments swath, differences in the amount of area covered on the wsp will reflect the amount spray droplets moving away from the swath.  The percent area coverage for each nozzle treatment for the wsp positioned 1, 2, and 3 meters downwind are compared and presented in table 1 and figure 1. Figures 2, 3, and 4 are included to highlight the differences at each collector location.  LSD’s for each wsp location are plotted.  Figure 5 and 6 provides information for comparing the four groups of nozzles tested.

The percent area coverage generated by DropletScan( for each nozzle treatment at the 1-meter location downwind ranges from 98.7 to 8.4 percent.  The traditional flat-fan nozzle types and the hollow cone (MC 1.875) all show significantly higher coverage amounts (LSD = 12.7) than the other nozzle styles or groups.  The nozzle types with less coverage represent designs for reducing spray drift with the venturi types showing the least downwind coverage.  The preorifice and chamber style nozzles exhibited less coverage on the collectors than the nozzles in group 1 but more than the group 4 nozzles. Very little differences were evident within the venturi group except for the Air Bubble (ab11004).  The ab11004 had 35.7 percent area coverage (LSD = 12.7) when compared to the AVI 11104 (20.9%), AI11004 (18.7%), TD04-XR11004 (17.8%), RU-4CP (16.0%), TD04-TT11004 (15.2%), and ULD120-04 (9.4%).  The group mean was 20.2 percent area coverage.  The ULD120-04 had the least amount of coverage for the venturi group of nozzles.  The chamber style turf flood had the least amount of coverage (8.4%) compared to all nozzles in the study.

Similar trends are found at the 2 and 3-meter downwind locations (figure 3 and 4).  As distance from the nozzle increased the amount of coverage decreased.  Within the flat-fan group (XR and TR), the 110-degree fan angle exhibited more coverage at the farther distances than the 80-degree versions.  Designs to reduce the development of smaller spray droplets, as in groups 2 and 4, exhibited less coverage with differences less significant at the second and third collector positions.

Individual nozzles means within each group are reported in figure 5 with a summary of group means shown in figure 6.  The group 1 nozzles had the most coverage (90.4%) at 1-meter.  The two nozzles in group 3 were next highest (72.3%); followed by group 2 nozzles (42%) and then the group 4 nozzles had the least amount of coverage (20.2%).  This trend was true at all three locations downwind.

Conclusions

Comparisons of the twenty-two nozzles types show a wide variation in the percent area coverage on the wsp downwind from the swath.  The highest amount of coverage and potential for spray drift occurred with the traditional flat-fans and the MC 1.875 hollow cone tip.  The preorifice and turbulation designs were significantly lower in coverage when compared to the flat-fan nozzle types.  The nozzles in group 2 exhibit a significant degree of difference within the group ranging from 72-8.4 percent coverage.  The two hollow cone designs were significantly different in coverage from each other (91.6 – 53%).  The nozzles in group 4 were overall the best for reducing the amount of downwind movement of spray droplets which is evidenced by the dramatically reduced amounts of coverage on the collectors.

The data in this study would support that certain nozzle designs will minimize the creation of small spray droplets.  In this study with all the variables held constant including the wind speed significant differences are present for drift potential.  Nozzles with the least amount of coverage on the water sensitive papers downwind would be considered good choices for reducing the drift potential.

## Acknowledgements

I would like to acknowledge the Manhattan, KS USDA-ARS Wind Erosion Research Unit staff for their support and use of the wind tunnel to complete this study.  I would also like to acknowledge the companies providing nozzles for use in this evaluation.

References

Gobel, B and Pearson, S. 1993.  Drift Reduction by spray nozzle techniques.   Second International Symposium on Pesticide Application Techniques.  219-226.

Mathews, G.A.  1992.  Pesticide Application Methods, 2nd Ed.  New York: Longman Scientific & Technical.

Miller, P.C.H. 1993.  Spray drift and its measurement.  In: Application Technology for Crop Production.  Matthews, G.A. and E.C. Hilsop, eds. London, CAB International.

Ozkan, H.E. and R.C. Derksen. 1998.   Extension Fact Sheet – Effectiveness of Turbodrop and Turbo TeeJet Nozzles in Drift Reduction.  The Ohio State University, Food, Agricultural and Biological Engineering Department. AEX 524-98.

Phillips, J.C. and P.C.H. Miller.  1999.  Field and Wind Tunnel Measurements of the Airborne Spray Volume Downwind of Single Flat-Fan Nozzles.  72. 161-170.

SDTF, 1997.  A Summary of Ground Application Studies, Stewart Agricultural Research Services, Inc.  P.O. Box 509, Macon, MO. 63552.

Smith, D.B., L.E. Bode, and P.D. Gerard.  2000.  Predicting Ground Boom Spray Drift.  Trans. ASAE 43(3):547-553.

Syngenta.  2002.  Water-sensitive paper for monitoring spray distributions.  CH-4002.  Basle, Switzerland: Syngenta Crop Protection AG.

Williams, W.L., D.R. Gardisser, R. E. Wolf,  and R. W. Whitney. 1999.  Field and Wind Tunnel Droplet Spectrum Data for the CP Nozzle.  ASAE Paper No. AA99-007.  St Joseph, MI.: ASAE.

Wolf, R.E., D.R. Gardisser, and W. L. Williams, 1999.  Spray Droplet Analysis of Air Induction        Nozzles Using WRK DropletScan(  Technology.  ASAE Paper No. 991026.   St. Joseph, MI.: ASAE.

Wolf, R., D. Peterson, and C. Minihan. Dec. 1999.  Comparisons of off-target deposits for conventional postemergence spray nozzles and venturi nozzles.  Proceedings North Central Weed Science Society.  54:70.

Wolf, R., 2000.  Fact Sheet - Equipment to Reduce Spray Drift.  Application Technology Series. Biological and Agricultural Engineering Dept., Kansas State University.  MF-2444.

Wolf, R., 2000. The Influence of Changing Application Volumes on Droplet Size Using Blended Pulse Spraying Technology.  ASAE Paper No. 001122.  St. Joseph, MI.: ASAE.

Wolf, R., D. Peterson, and C. Minihan.  Dec. 2000.  Influence of Spray Droplet Size On Paraquat and Glyphosate Efficacy. Proceedings North Central Weed Science Society.  55:116-17.

Wolf, R. and C. Minihan.  March 2001, Comparison of Drift Potential for Venturi, Extended Range, and Turbo Flat-fan Nozzles.  ASAE Paper No. MC01-108.  St. Joseph, MO.: ASAE Sponsored.

Wolf, R., D. Peterson, and C. Minihan.  Dec. 2001.  Influence of Nozzle Type and Spray Pressure on Droplet Size. Proceedings North Central Weed Science Society. 56:Paper No. 142.

Womac, A.R., J.C. Goodwin, and W.E. Hart. 1997. Tip Selection for Precision Application of Herbicides, University of Tennessee CES. Bulletin 695.

Table 1.  Nozzle types evaluated with group, company, and spray pattern style.

| Nozzle Type* | Group** | Company | Pattern Style |
| --- | --- | --- | --- |
| XR8004 | 1 | Spraying Systems | Flat-fan |
| XR10004 | 1 | Spraying Systems | Flat-fan |
| TR80-04 | 1 | Hypro | Flat-fan |
| TR110-04 | 1 | Hypro | Flat-fan |
| DG11004 | 2 | Spraying Systems | Preorifice Flat-fan |
| RF4 | 2 | Delavan | Preorifice Flat-fan |
| TKVS2 | 1 | Spraying Systems | Flooding Flat-fan |
| TFVP2 | 2 | Spraying Systems | Chamber Flooding Flat-fan |
| TFVS2 | 2 | Spraying Systems | Chamber Flooding Flat-fan |
| TTJ04 | 2 | Spraying Systems | Chamber Turf Flooding Flat-fan |
| TT11004 | 2 | Spraying Systems | Chamber Flat-fan |
| AI11004 | 4 | Spraying Systems | Venturi Flat-fan |
| TD04-XR11008 | 4 | Greenleaf/Spraying Systems | Venturi Flat-fan |
| AIR MIX 110-04 | 4 | Greenleaf | Venturi Flat-fan |
| ULD 120-04 | 4 | Hypro | Venturi Flat-fan |
| AB11004 | 4 | Air Bubble Jet- ABJ Agri Products | Venturi Flat-fan |
| RAINDROP ULTRA 4 | 4 | Delavan/CP | Venturi Flat-fan |
| AVI110-04 | 4 | Hypro/Albuz | Venturi Flat-fan |
| DR80-04 | 2 | Wilger | Preorifice Flat-fan |
| TD04-TT11004 | 4 | Greenleaf/Spraying Systems | Venturi Flat-fan |
| RA4 | 3 | Delavan | Hollow Cone |
| MC1.875 | 3 | Great Plains | Hollow Cone |
| * All nozzles were calibrated to spray at 1.5 liters per minute at 276 kPa ** Groups: 1 = Traditional flat-fan; 2 = preorifice and/or chamber; 3 = hollow-cone; 4 = venturi |

Table 2.  Coverage means for all nozzle types by nozzle, by group, and group mean*.

|  | WSP all locations | WSP location – 1 meter |
| --- | --- | --- |
| Nozzle Type | 1 meter | 2 meters | 3 meters | Group1 | Group 2 | Group 3 | Group 4 | Group |
| tr8004 | 98.7 | 83.0 | 28.4 | 98.7 |  |  |  |  |
| tr110-04 | 97.3 | 94.8 | 63.2 | 97.3 |  |  |  |  |
| xr8004 | 92.7 | 60.4 | 22.1 | 92.7 |  |  |  | 1 = 90.4 |
| mci1.875 | 91.2 | 68.1 | 26.9 |  |  | 91.2 |  |  |
| xr11004 | 90.1 | 66.1 | 27.1 | 90.1 |  |  |  |  |
| tkvs2 | 72.4 | 54.1 | 26.8 | 72.4 |  |  |  | 2 = 42.0 |
| dg11004 | 72.0 | 57.4 | 20.0 |  | 72.0 |  |  |  |
| tt11004 | 64.6 | 35.2 | 16.7 |  | 64.6 |  |  |  |
| ra4 | 53.0 | 12.1 | 3.7 |  |  | 53 |  | 3 = 72.3 |
| tfvp2 | 50.7 | 33.4 | 15.2 |  | 50.7 |  |  |  |
| tfvs2 | 43.6 | 27.1 | 13.7 |  | 43.6 |  |  |  |
| ab11004 | 35.7 | 14.4 | 3.9 |  |  |  | 35.7 |  |
| dr80-04 | 30.2 | 8.9 | 2.6 |  | 30.2 |  |  |  |
| am110-04 | 27.1 | 9.9 | 3.1 |  |  |  | 27.1 |  |
| rf4 | 24.6 | 11.2 | 4.2 |  | 24.6 |  |  |  |
| avi110-04 | 20.9 | 8.0 | 3.0 |  |  |  | 20.9 |  |
| ai11004 | 18.7 | 8.7 | 2.3 |  |  |  | 18.7 |  |
| td04-xr11008 | 17.8 | 7.1 | 2.0 |  |  |  | 17.8 | 4 = 20.2 |
| ru-4cp | 16.0 | 7.8 | 2.7 |  |  |  | 16.0 |  |
| td04-tt11008 | 15.2 | 4.8 | 1.7 |  |  |  | 15.2 |  |
| uld120-04 | 9.4 | 4.1 | 1.2 |  |  |  | 9.4 |  |
| ttj04 | 8.4 | 3.1 | 1.1 |  | 8.4 |  |  |  |

*Percent area coverage on water sensitive papers.  Higher coverage percentages indicate more potential for spray drift.

Figure 1.  Coverage means for all nozzle types at all locations.

Figure 2.  Means at 1-meter downwind for all nozzle types.  LSD=12.7.

Figure 3.  Means for all nozzle types at 2 meters downwind.   LSD=15.6.

Figure 4.  Means for all nozzle types at 3-meters downwind.   LSD=7.0.

Figure 5.  Coverage by group at 1-meter.

Figure 6. Group mean coverage at 1-meter.