## Slide 1: BASF Project – Meade, KS July 28, 2009
Spray Solution Effects on Fungicide Application to Corn

## Slide 2: Meade, KS

## Slide 3: Materials and Methods:
AT 401(Bringham Flying Service, Craig Stratton - Pilot)
  Drop booms
  CP-09 (29 - .078 and 9 - .125) w/5° deflection
  36 PSI
  67 foot swath, 120 mph ground speed by GPS
  Droplet spectrum - Medium
Aircraft calibrated for 3 GPA

## Slide 4: Treatments
Trt # | Treatment1 |  | Rate/Acre
1 | Headline EC + water + Vision Pink2 | COC | 6 oz + 16 oz
2 | Untreated check |  | 
3 | Headline SC + water + Vision Pink2 | COC | 6 oz + 16 oz
4 | Untreated Check |  | 
5 | Headline SC + Caramba + water + VP | X | 5.8 oz + 6.1 oz
6 | Untreated check |  | 
7 | Quilt + water + Vision Pink2 | COC | 14 oz + 16 oz
1All treatments were applied at 28 L/Ha (3 GPA) using tap water.
2Vision Pink added at 1 quart (16 oz) per 50 gallons of water.

## Slide 6
Untreated Check
Untreated Check
Untreated Check
Headline EC (6 oz/ac) + COC (1 pt/ac)
Headline SC (6 oz/ac) + COC (1 pt.ac)
Quilt (14 oz/ac) + COC (1 pt/ac)
Headline SC (5.8 oz/ac) + Caramba (6.1 oz/ac)
N
1
3
5
7

## Slide 8
Chart: % Area Coverage by Location on Plant
| Headline EC + COC | Headline SC + COC | Headline SC + Caramba | Quilt + COC
bottom | 0.48 | 0.69 | 0.09 | 0.21
middle | 1.12 | 1.64 | 0.2 | 0.25
top | 1.59 | 2.32 | 0.57 | 0.27
total | 3.19 | 4.65 | 0.86 | 0.73

## Slide 9
Chart: No Canopy - % Area Coverage
| Headline EC + COC | Headline SC + COC | Headline SC + Caramba | Quilt + COC
No Canopy | 2.58 | 2.73 | 3.53 | 2.81
Chart: VMD with No Canopy
| Headline EC + COC | Headline SC + COC | Headline SC + Caramba | Quilt + COC
No Canopy | 344 | 361 | 337 | 346

## Slide 10
Chart: % Disease Control
| Headline EC | Headline SC | Headline + Caramba | Quilt
8/14/2009 | 80.7 | 92.1 | 90 | 92.9
9/4/2009 | 88.6 | 87.1 | 58.6 | 40
9/23/2009 | 72.1 | 54.3 | 48.6 | 54.3
Chart: % Disease Damage
| Check | Check | Check
8/14/2009 | 32.9 | 11.4 | 20
9/4/2009 | 88.6 | 67.1 | 25
9/23/2009 | 68.6 | 88.6 | 97.1

## Slide 11
Chart: Yield
| Headline EC + COC | check | Headline SC + COC | check | Headline SC + Caramba | check | Quilt + COC
 | 264 | 261 | 259 | 269 | 273 | 270 | 271
APEX Farm Management Software

## Slide 12: Summary
Differences were found in coverage among treatments within the corn canopy.
Treatments had little effect on droplet size
Yield differences were minimal.
Disease control varied by treatment, timing, and field location.
Damage from disease increased over time.

## Slide 13: Treatment VMD’s:
Chart: Treatment VMD
| Tap Water 1 | Superb HC + Interlock | Formula 1 | #PX056-Z | Tap Water 2 | AG 06037 | AG 08050 | Interlock 1.25 | Control | Tap Water 3 | INT 908 | Tap Water + oil | Interlock 0.8
VMD | 374 | 380 | 398 | 393 | 345 | 331 | 333 | 348 | 336 | 368 | 356 | 347 | 379