## Slide 1
NAAA/ASABE
Technical Session
Robert E. Wolf
Associate Professor - Extension Specialist Application Technology
Biological and Agricultural Engineering
Utilization of Additives to help Reduce Drift Potential

## Slide 2: Drift Reduction Additives:
Many available!
Not EPA regulated
Long chain polymers
Soluble powders
Reduction in off-target movement documented
Not all will work!!!!
Pump shear problems
Effect on the pattern?
Deposition Aids

## Slide 3
Chemical Producers & Distributors Association

## Slide 4: Field Analysis of Drift Reducing Adjuvants…..deposition aids.
Goodland, KS – 2002
Burdett, KS - 2008

## Slide 5: Participants in the Study:
41-A
Formula One
AMS 20/10
Border EG 250
Control
INT VWZ
Inplace
Garrco Exp-3
INT YAR
Border XTRA 8L
HM2005-C
HM0226
Liberate
Target LC
HM2052
INT HLA
HM 0230
Valid
Double Down
20 & 21. water
United Suppliers
Helena Chemical
Garrco
Loveland
Wilber-Ellis
Rosen’s
Precision Labs
SanAg
Companies
Products
Some worked & some didn’t!!!

## Slide 6
Product Name | Product Company | Mixing ratea
Tap water 1 | Local supply | X-77 only
Superb HC + Interlock | Winfield Solutions | 133 oz + 33 oz / 50 gal
Formula 1 | United Suppliers | 1.5 qt / 50 gal
#PX056-Z | Precision Labs, Inc | 5 qt / 50 gal
Tap water 2 | Local supply | X-77 only
Ag 06037 | Winfield Solutions | 64 oz / 50 gal
Ag 08050 | Winfield Solutions | 80 oz / 50 gal
Interlock 1.25 | Winfield Solutions | 80 oz / 50 gal
Control | GarrCo Products, Inc | 2 oz /50 gal
Tap water 3 | Local supply | X-77 only
INT 908 | Rosen’s | 5 gal / 45 gal
Tap water + Prime Oilb | Local supply + Winfield Solutions | 266 oz / 50 gal
Interlock 0.8 | Winfield Solutions | 50 oz / 50 gal
a All tank mixes included X-77 at .25% v/v (16 ounces per 50 gallon load).
bOil to simulate a suggested tank mix with fungicide (Prime Oil @ 1 pint/acre).

## Slide 7: Materials and Methods (2008):
AT 502A(Rucker Flying Service)
  Drop booms
  CP-11TT #15 straight stream nozzles w/8° deflection
  44 PSI
  156 mph ground speed by GPS
  Droplet spectrum: Medium, %volume <200 = 7.65%
Aircraft calibrated for 3 GPA

## Slide 10: Weather Data:
Sept. 4, 2008 from 10:00am – 1:45pm
Wind speed range: 6.3 – 8.8 MPH
Average wind speed: 7.8 MPH
Temperature: 67.2 F
Humidity: 44.9%

## Slide 11: Treatment VMD’s:
Chart: Treatment VMD
| Tap Water 1 | Superb HC + Interlock | Formula 1 | #PX056-Z | Tap Water 2 | AG 06037 | AG 08050 | Interlock 1.25 | Control | Tap Water 3 | INT 908 | Tap Water + oil | Interlock 0.8
VMD | 374 | 380 | 398 | 393 | 345 | 331 | 333 | 348 | 336 | 368 | 356 | 347 | 379

## Slide 12: Horizontal Drift Summary:
Chart: 
| Tap Water 1 | Superb HC + Interlock | Formula 1 | #PX056-Z | Tap Water 2 | AG 06037 | AG 08050 | Interlock 1.25 | Control | Tap Water 3 | INT 908 | Tap Water + oil | Interlock 0.8
Column1 | 44.1604 | 50.1586 | 42.867 | 47.7448 | 42.6844 | 54.0475 | 55.7955 | 41.0916 | 33.9195 | 39.8196 | 32.8623 | 35.694 | 35.0574
abc
abc
abcd

## Slide 13: Vertical Drift Summary:
Chart: 
| Tap Water 1 | Superb HC + Interlock | Formula 1 | #PX056-Z | Tap Water 2 | AG 06037 | AG 08050 | Interlock 1.25 | Control | Tap Water 3 | INT 908 | Tap Water + oil | Interlock 0.8
Column1 | 5.9095 | 11.3307 | 10.4683 | 15.7419 | 14.983 | 17.3733 | 18.8222 | 12.8129 | 3.8192 | 4.2332 | 3.6584 | 5.91 | 2.7118
ab
bc
bc
cde
cde
de
e
cd
a
a
a
ab
a

## Slide 14: Vertical Drift Profile:
Chart: Vertical Coverage at Altitude
| VO | V5 | V10 | V15 | V20 | V25 | V30 | V35 | V40
Coverage | 10.4738 | 17.9109 | 20.2143 | 20.0818 | 17.5064 | 14.788 | 11.4643 | 8.4707 | 6.8525

## Slide 15: Total Drift Summary:
Chart: 
| Tap Water 1 | Superb HC + Interlock | Formula 1 | #PX056-Z | Tap Water 2 | AG 06037 | AG 08050 | Interlock 1.25 | Control | Tap Water 3 | INT 908 | Tap Water + oil | Interlock 0.8
Series 1 | 50.0699 | 61.4893 | 53.3353 | 63.4867 | 57.6674 | 71.4208 | 74.6177 | 53.9045 | 37.7387 | 44.0527 | 36.5207 | 41.604 | 37.7693
bcd
cde
ef
ef
de
fg
g
cde
a
abc
a
ab
a

## Slide 16: Total Drift Ranked:
Chart: 
| INT 908 | Control | Interlock 0.8 | Tap Water + oil | Tap Water 3 | Tap Water 1 | Formula 1 | Interlock 1.25 | Tap Water 2 | Superb HC + Interlock | #PX056-Z | AG 06037 | AG 08050
Series 1 | 36.5207 | 37.7387 | 37.7693 | 41.604 | 44.0527 | 50.0699 | 53.3353 | 53.9045 | 57.6674 | 61.4893 | 63.4867 | 71.4208 | 74.6177
a
cde
de
ef
ef
fg
g
a
a
abc
ab
bcd
cde
water average

## Slide 17: Summary
Differences among treatments in coverage representing downwind drift were found at all vertical and horizontal collector locations.
Some products provided significant drift reduction benefits when compared to others.
Many of the products did not provide any drift reduction when compared to water.
Based on mixing, loading, and system cleanout evaluations, some products may hinder good application techniques.

## Slide 18: Acknowledgements:
Cary and Jane Rucker
Participating Companies and Reps
Kansas Department of Ag

## Slide 19
www.bae.ksu.edu/faculty/wolf/
Thanks!
For more information contact:
rewolf@ksu.edu