Paper Number: 02-AA07

An ASAE Meeting Presentation

Practical Field Demonstrations for Drift Mitigation

Robert E. Wolf

Biological and Agricultural Engineering Dept., 229 Seaton Hall, Manhattan, KS 66506.

Dennis R. Gardisser

Biological and Agricultural Engineering Dept., University of Arkansas CES,

PO Box 391, Little Rock, AR 72203

Cathy L. Minihan

Department of Agronomy, 2017D Throckmorton Hall, Manhattan, KS 66506

Written for presentation at the

2002 ASAE NAAA/ASAE Technical Session

36th Annual National Agricultural Aviation Association Convention

Silver Legacy Hotel and Casino, Reno, Nevada, USA

December 9-12, 2002

Abstract. A field study was conducted to determine the influence of adding spray drift control/deposition aid products to tank mix solutions for fixed wing aerial applications.  Two agricultural aircraft, an Air Tractor 502A and a Cessna 188 Ag Husky, were used to apply treatments at 28 l/ha with 21 different products.  Each aircraft was configured to simulate a typical herbicide application scenario representative of its design and style.  Downwind horizontal and vertical drift characteristics were evaluated for each product.   Preliminary results of the study show that drift control/deposition aid products added to the tank mix do affect the amount of horizontal and vertical spray drift, for the application scenarios and operating conditions used.  Preliminary results indicate that several products tended to result in more downwind deposits when compared to water while others reduced the amount of downwind drift deposits.  Caution is presented that a full statistical analysis of the wind affect has not been factored into the results and may alter the findings reported for some of the products.  The significance of the differences is not know at this time.

Keywords. Aerial application, drift, drift minimization, droplet size, spray, drift control products, deposition aids

Introduction

Controlling or minimizing the off-target movement of sprayed crop protection products is critical. Researchers have conducted numerous studies over time to better understand spray drift problems.  Particularly, a recent group of studies conducted by the industries Spray Drift Task Force (SDTF, 1997) generated numerous reports to support an Environmental Protection Agency (EPA) spray drift data requirement for product reregistration and future label guidance statements on drift minimization.

Even though a better understanding of the variables associated with spray drift exists, it is still a challenging and complex research topic.  Environmental variables, equipment design issues, many other application parameters, and all the interactions make it difficult to completely understand drift related issues (Smith, et al., 2000).  Droplet size and spectrum has been identified as the one variable that most affects drift (SDTF, 1997).  Many forces impinge on droplet size, but it is still the drop size that must be manipulated to optimize performance and eliminate associated undesirable results (Williams, et al., 1999).  Drift is associated with the development of high amount of fine droplets (Gobel and Pearson, 1993).

Off-target drift is a major source of application inefficiency.   Application of crop protection products with aerial application equipment is a complex process.  In addition to meteorological factors, many other conditions and components of the application process may influence off-target deposition of the applied products (Threadgill and Smith, 1975; Kirk et al., 1991; Salyani and Cromwell, 1992).  Spray formulations have been found to affect drift from aerial applications (Bouse et al., 1990).  Materials added to aerial spray tank mixes that alter the physical properties of the spray mixture affect the droplet size spectrum. (SDTF, 2001).  With new nozzle configurations and higher pressure recommendations (Kirk, 1997), and with the continued development of drift reducing tank mix materials, applicators seek to better facilitate making sound decisions regarding the addition of drift control products into their tank mixes.

# Objective

The objective of this study was to evaluate the influence of selected drift control products/deposition aids on horizontal and vertical spray drift during two selected fixed wing aerial application scenarios.

# Materials and Methods

A field study was conducted to determine the influence on reducing drift when selected tank mix drift control products/deposition aids were added to the spray tank during fixed wing aerial applications. Two aircraft with different application scenarios were used to make the comparisons.  One of the fixed wing aircraft, an Air Tractor 502A (Air Tractor Inc., Olney, Texas), was equipped with drop booms; CP-09 Straight Stream nozzles (CP Products, Inc., Mesa, Arizona) with no deflection; using a combination of .078 and .125 orifice settings;  and spraying at 276 kPa (40 psi). The second, a Cessna 188 Ag Husky (Cessna Aircraft Co., Wichita, KS), was equipped with Ag-Tips (Ag-Tips, Arrowwood, Alta, Canada); CP-03 nozzles with .078 orifice settings and a 30-degree deflector; and was spraying at 220 kPA (32 psi).  The AT 502A flew at a ground speed 241 km/h (150 MPH) and the Cessna 188 flew at 185 km/h (115 MPH).  Pilots were instructed to use an application height of 3-3.7 m (10-12 feet).  Both aircraft made all treatments.

The study was conducted on September 25 and 26, 2002 at the Goodland airport in Goodland, Kansas.  The study area was flat, open and dry with a 15-25 cm (6-10 inches) desert-like grass and weed canopy.  Twenty-one different products (two were water only) were evaluated in three replications using the two airplanes.  All products and both airplanes were completely randomized over both days of the study.  There were 121 treatments evaluated.  Spray mixes containing 560 liters (60 gal) of tap water, X-77 Spreader (Loveland Industries, Greeley, Colorado) at 0.25% volume/volume, and individual drift control additives/deposition aids were applied at 28 L/ha (3 GPA).  All tank mix treatments were prepared based on recipes provided by each participating company (see appendix A).  Temperature, relative humidity, and maximum and average wind velocities were recorded using Kestrel 3000 (Nielson-Kellerman, Chester, PA) hand-held instruments averaged during the time of application for each treatment. To minimize tank mix contamination between treatments, a hot water-high pressure washer was used to facilitate hopper cleanout.  Water was included on both days of the study as a check.

Spray drift deposits were collected for measurement and analysis using horizontal collectors, a drift tower with vertical collectors, and 2.5 X 7.6 cm  (1 X 3 inch) water sensitive paper (WSP) (Spraying Systems Company, Wheaton, Illinois).  To collect the horizontal drift, WSP (card) was placed on 2.5 X 10 cm blocks sloped toward the flight line and placed downwind from the flight line along the drift line at 15.25 m (50 feet) increments to a distance of 106.75 m (350 feet).  A total of seven horizontal cards were collected for each treatment (H50, H100, H150, H200, H250, H300, and H350).  A retractable tower capable of extending to 12.2 m (40 feet) and designed to hold WSP at 1.53 m (5 feet) increments was used for the vertical drift collection.  A total of nine vertical cards were collected for each treatment (V0, V5, V10, V15, V20, V25, V30, V35, and V40).  The collector layout is shown in Appendix B.  Each treatment included four parallel back and forth passes along the flight line for a minimum distance of 213.5 m (700 feet), 106.75 m (350 feet) before and after the drift collection line.  Marker flags were positioned along the flight line to assist the pilot in locating the flight line and with the spray timing.  To facilitate timing and shorten the duration of the study two identical drift collection stations were used to simulate the repetitions.  Collection station I was used to record data for each treatment as replication 1 and 3.  Collection station II was used for all treatments representing replication 2.  As test airplane 1 cycled through the collector stations (3 replications of 4 passes), airplane 2 was being rinsed and readied for the next test treatment. Each 3-rep treatment took approximately 20 minutes.  Except for a wind delay on day 1 and a brief rain shower on day 2 the collection process preceded smoothly.  All treatments were applied in a crosswind.  The crosswind average speed averaged for the two days was 11.9 Km/h (7.4 mph).  The average for the maximum wind speeds was 17.1 Km/h (10.6 MPH).  Crosswind average was used in the analysis for this report.  The collector system was easily shifted to maintain the 90-degree crosswind for each treatment.  Wind direction was monitored by observing a flag and ribbon placed at the top of the tower.  Average temperature for the two days was 12.7C (55F).  Average humidity was 50 percent.

After each replication, the collection cards were placed in prelabeled-sealable bags for preservation.  Data envelopes were used to organize and store the cards until analysis was complete.  DropletScan( (WRK of Arkansas, Lonoke, AR; and WRK of Oklahoma, Stillwater, OK; Devore Systems, Inc., Manhattan, KS) was used to analyze the cards.

Spray droplet stains collected on water sensitive paper are a good indicator of spray drift when comparing the amount of coverage obtained on the cards (Wolf et al., 1999, Wolf and Frohberg 2002).  Since the cards are placed outside and downwind from each treatments target area, differences in the amount of area covered on the card will reflect the amount of drift.  For this study, the percent area coverage and spray deposition rate (GPA) for the horizontal and vertical drift profiles were used as a means to separate differences in treatments.  There were 2,016 water sensitive cards analyzed by DropletScan( in this study.

Statistical analyses of the data were conducted with SAS 8.2 (SAS, 2001).   The initial model used was a General Linear Model (GLM) procedure to analyze the water sensitive paper data by horizontal and vertical distance.  The average crosswind speed was used as a covariate to account for deviation in wind velocity during each treatment.  The LS Means for each product were tested and used to report the differences found at each horizontal and vertical distance.  Additional models will be used to further separate differences and analyze the covariate, wind.  Due to the timing of this study and the large amount of data to analyze, the findings reported in this study are preliminary and will be subject to adjustments in a final report.

Results and Discussion

Preliminary summary data from the field study are shown in Tables 1-4 with the graphical representation of the same data shown in Figures 1-6.  Because of the range of the deposits through the collector distance, a single graphical display does not facilitate observing the differences that may exist between products.  Also, the presence of heavy deposits on the first horizontal (H50) collector position is likely to be the result of wind blown swath displacement.  Even with the swath displacement consideration, differences at the H50 location in drift control/deposition aid products are evident.  Because of time constraints a full statistical analysis of the results are not available here.  General overviews of the trends are reported.  It is quite possible that much of the data will be altered after the full statistical model is run correcting for the wind variability.

In the initial statistical analysis, the products were compared by averaging across both airplanes at each sample location.  LS means are used to estimate differences.  Using an average of the two water treatments as a reference, products that contained more deposition and coverage at the horizontal sample locations (H50-H350) can be differentiated from those that had less deposition and coverage.  With some variability at all horizontal locations, approximately 40-60 percent of the products show more gallons per acre deposited and more percent area coverage when compared to the water treatments as a baseline.   The remaining products were measured with less deposits.

Vertical measurements taken from the tower collectors present some interesting findings.  Except for in a limited number of treatments, deposition and coverage amounts were measured for all products for all nine collector positions (V0-V9).  Refer to tables 3 and 4 and figures 5 and 6 to review this data.  As was indicated with the horizontal measurements, in general, approximately 40-60 percent of the products had more deposition and coverage than the averaged water treatments.  The remainder would be less.  Differences in volume median diameter (VMD) on the vertical collectors were averaged across product comparing the effect of airplane.  The VMD for the Cessna 188 (158 microns) was significantly larger than the VMD for the Air Tractor 502A (138 microns).

Another factor to include in evaluating each product relates to considerations given to the mixing, loading, and tank cleanout properties.  Observations recorded during the mixing and loading phase of this study indicate that certain products exhibited characteristics that may hinder good application techniques.  Products A, E, F, J, P were noted as difficult to mix with A and P indicated as hanging up in the tank.  Products E, F, and P were noted to form globules in the tank.  Product F was noted for being difficult to get clean from the system.  Since a high-pressure/hot-water system was used to clean the tank and booms, most products were not noted as difficult to remove from the system.

Tank mix samples were collected for each treatment.  Theses sample are planned for a spread factor analysis.  Spread factor information will then be used to further analyze the differences reported in this study.

Conclusions

## This study was conducted to determine the influence of drift control/deposition aid products on crosswind drift from practical aerial applications using fixed wing aircraft.  An Airtractor 502A and a Cessna 188 were used to apply the treatments.  Differences in products are shown at all horizontal and vertical collector positions.  Deposition and coverage variability for each product indicate that wind speed fluctuation is a major factor in this study.  Preliminary results show that many of the products did not provide any benefits for drift reduction.   A few of the products exhibited the potential to reduce the amount of drift.  Until the final statistical analysis is used to factor out the wind variability no final conclusion on product comparisons can be made.  The researchers are confident that the final results in this study will provide useful information to aerial applicators regarding decisions they need to make about drift control/deposition aid products.

## Future Data Analysis

The next step in the data analysis will be to explore the data through additional models of the covariate analysis procedure relating wind speed to horizontal and vertical drift deposits over distance.  In addition to product comparisons, differences in airplanes will be analyzed.

## How to find final results from this study!!!

## The final results of this study will be published on the following web site.  Please monitor for that announcement.  Future publications will be forthcoming as data analysis is completed.

http://www.bae.ksu.edu/rewolf/

## Acknowledgements

Special appreciation is expressed to Cary Rucker, Rucker Flying Service, Inc., Burdette, KS, and Dave Faust and Bill Ashton, from Hawkeye Flying Service, Inc, Goodland, KS, for the donation of their aircraft and time to this study.  Also, we would like to express thanks to the Goodland Airport, Renner Field, and Butterfly Aviation for providing the space to set up the tests and to analyze the data from the study.  Appreciation is also expressed to Barker Farm Services, Dan and Beverly and crew, for the use of their hanger and equipment to facilitate the efficient mixing and loading of the various treatments used in the study.  We would especially like to thank the participating companies for their generous donations of product, time, and funds to support this study.  A special thank you is offered to Spraying Systems Company for their support in providing the water sensitive paper used to collect the drift. We would like to thank Richard Whitney for the use of his analysis equipment and time in support of this project.  We are also very grateful to the many, many people providing technical support with sample collection, processing, and data compilation.  The food and beverage donors were also very much appreciated.  Without the commitment of the people, who were representing the participating companies, the Kansas Agricultural Aviation Association, the Cooperative Extension Service, and others, this study would have been impossible to complete in a practical and efficient manner.

References

Bouse, L.F., I.W. Kirk, and L.E. Bode.  1990.  Effect of spray mixture on droplet size.  Transactions of ASAE 33(3):783-788.

Gobel, B and Pearson, S. 1993.  Drift Reduction by spray nozzle techniques.   Second International Symposium on Pesticide Application Techniques.  219-226.

Kirk, I.W.  1997.  Application parameters for CP nozzles.  Presented at 1997 Joint ASAE/NAAA Technical Meeting, Paper No. AA97-006.  ASAE, 2950 Niles Road, St. Joseph, MI  49085.

Kirk, I.W., L.F. Bouse, J.B. Carlton, and E. Franz. 1991.  Aerial application parameters influence spray deposition in cotton canopies.  Presented at 1991 Joint ASAE/NAAA technical Meeting, Paper No. AA91-007.  ASAE, 2950 Niles Road, St. Joseph, MO  49805.

Salyani, M. and R.P. Cromwell. 1992.  Spray Drift from ground and aerial application.  Transactions of ASAE 35(4):1113-1120.

SDTF, 1997.  A Summary of Ground Application Studies, Contact David R. Johnson at Stewart Agricultural Research Services, Inc.  P.O. Box 509, Macon, MO. 63552.

SDTF. 2001.  A Summary of Tank Mix and Nozzle Effects on Droplet Size.  Spray Drift Task Force.  Contact David R. Johnson at Stewart Agricultural Research Services, Inc., P.O. Box 509, Macon, MO  63552.

Smith, D.B., L.E. Bode, and P.D. Gerard.  2000.  Predicting Ground Boom Spray Drift.  Trans. ASAE 43(3):547-553.

Threadgill, E.D. and D.B. Smith, 1975.  Effect of physical and meteorological parameters on drift of controlled-size droplets.   Transactions of ASAE 18(1):51-56.

Williams, W.L., Gardisser, D.R., Wolf, R.W., and Whitney, R.W., Field And Wind Tunnel Droplet Spectrum Data For The CP Nozzle, Presented at the 1999 Joint ASAE/NAAA technical meeting, Paper No. AA99-007. ASAE, 2950 Niles Road, St. Joseph, MO 49805

Wolf, R.E., Gardisser, D.R., and Williams, W.L., Spray Droplet Analysis of Air Induction Nozzles Using WRK DropletScan™ Technology, American Society of Agricultural Engineers, ASAE 991026, Toronto, Canada, July, 1999.

Wolf, R.E., D.D. Frohberg., Comparison of Drift for Four Drift-Reducing Flat-fan Nozzle Types Measured in a Wind Tunnel and Evaluated using DropletScan( Software, American Society of Agricultural Engineers, ASAE 021101, Chicago, IL, July, 2002.

Appendix

| Appendix A: Product Code Assignments |
| --- |
| Product Code | Product Name | Product Company | Mixing rate* |
| A | Formula One | United Suppliers, Inc | 3 qt/100 gal |
| B | HM0226 | Helena Chemical Company | 1% v/v |
| C | AMS 20/10 | United Suppliers, Inc | 10 lb/100 gal |
| D | Border EG 250 | Precision Laboratories, Inc | 10 oz/100 gal |
| E | Control | Garco Products, Inc. | 4 oz/100 gal |
| F | INT VWZ | Rosen’s, Inc. | 15 lb/100 gal |
| G | Inplace | Wilbur-Ellis Company | 8 oz/acre |
| H | Garco #3 | Garco Products, Inc. | 8 oz/100 gal |
| I | INT YAR | Rosen’s, Inc. | 9.0 lb/100 gal |
| J | Border Xtra 8L | Precision Laboratories, Inc. | 2.5% v/v |
| K | HM 2005-C | Helena Chemical Company | 9 lb/100 gal |
| L | Double Down | United Suppliers, Inc. | 2.5 gal/100 gal |
| M | Liberate | Loveland Industries, Inc | 1 qt/100 gal |
| N | Target LC | Loveland Industries, Inc | 2 oz/100 gal |
| O | HM 2052 | Helena Chemical Company | 1% v/v |
| P | INT HLA | Rosen’s, Inc | 1 lb/100 gal |
| Q | HM 0230 | Helena Chemical Company | 0.5% v/v |
| R | Valid | Loveland Industries, Inc | 1 pt/100 gal |
| S | Tap Water |  |  |
| S2 | Tap Water |  |  |
| T | 41-A | San-Ag | 2 oz/100 gal |

* All tank mixes included X-77 at .25% v/v.

Appendix B: Drift collector diagram.

|  |  |  | Wind direction |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Drift Tower |
|  |  |  | Vertical Tower Collectors |  |  |  |
|  |  |  | [V0-V40 feet] |  |  |  |
|  |  |  | Drift Sample Line |  |  |  |
|  |  |  |  |  |  | Weather Station |
|  |  |  | Horizontal Collectors |  |  |  |
|  |  |  | [H0-H350 feet] |  |  |  |
|  | flight line |  |  |  |  |  |
|  | [700 feet) |  |  |  |  |  |

Table and Figures

Table 1. LS Means for horizontal drift deposits recorded as gallons per acre on water sensitive paper for twenty-one products*.

|  | Feet |
| --- | --- |
| Product** | 50*** | 100 | 150 | 200 | 250 | 300 | 350 |
| A | 4.64 | 0.42 | 0.42 | 0.39 | 0.09 | 0.08 | 0.03 |
| B | 7.09 | 1.04 | 0.48 | 0.28 | 0.16 | 0.12 | 0.15 |
| C | 5.75 | 0.87 | 0.22 | 0.09 | 0.09 | 0.07 | 0.04 |
| D | 5.24 | 0.89 | 0.14 | 0.27 | 0.09 | 0.06 | 0.07 |
| E | 4.75 | 0.73 | 0.12 | 0.08 | 0.06 | 0.04 | 0.02 |
| F | 5.62 | 0.93 | 0.08 | 0.15 | 0.10 | 0.04 | 0.05 |
| G | 8.20 | 2.04 | 0.81 | 0.57 | 0.08 | 0.10 | 0.08 |
| H | 8.18 | 0.32 | 0.27 | 0.11 | 0.08 | 0.00 | 0.00 |
| I | 6.05 | 2.18 | 0.30 | 0.10 | 0.05 | 0.06 | 0.03 |
| J | 8.38 | 0.52 | 0.65 | 0.04 | 0.06 | 0.03 | 0.02 |
| K | 11.89 | 3.77 | 1.14 | 0.60 | 0.44 | 0.23 | 0.28 |
| L | 6.85 | 0.27 | 0.20 | 0.08 | 0.07 | 0.04 | 0.02 |
| M | 11.05 | 2.50 | 0.56 | 0.08 | 0.00 | 0.08 | 0.00 |
| N | 8.57 | 1.17 | 0.39 | 0.18 | 0.11 | 0.05 | 0.06 |
| O | 14.69 | 1.31 | 1.07 | 1.17 | 0.11 | 0.00 | 0.26 |
| P | 4.48 | 0.71 | 0.26 | 0.04 | 0.80 | 0.04 | 0.05 |
| Q | 6.64 | 0.83 | 0.34 | 0.24 | 0.01 | 0.13 | 0.06 |
| R | 7.89 | 2.22 | 0.49 | 0.33 | 0.10 | 0.12 | 0.05 |
| S | 6.19 | 1.06 | 0.20 | 0.09 | 0.16 | 0.02 | 0.08 |
| S2 | 7.81 | 1.74 | 0.41 | 0.20 | 0.08 | 0.07 | 0.06 |
| T | 5.74 | 0.88 | 0.20 | 0.07 | 0.06 | 0.03 | 0.02 |
| *Gallons per acre from scanned water sensitive paper - 2.54 X 7.62 cm. **Product code is located in Appendix A. ***Heavier amounts due swath displacement in wind. |

Figure 1. LS Means horizontal drift deposits recorded as gallons per acre on water sensitive paper for twenty-one products.

Figure 2. LS Means horizontal drift deposits on collectors at 50 – 350 feet downwind, recorded as gallons per acre on water sensitive paper for twenty-one products.  Scales are different to help separate differences.

Table 2. LS Means for horizontal drift deposits recorded as percent area coverage on water sensitive paper for twenty-one products*.

|  | Feet |
| --- | --- |
| Product** | 50*** | 100 | 150 | 200 | 250 | 300 | 350 |
| A | 12.41 | 1.26 | 1.20 | 0.64 | 0.27 | 0.30 | 0.10 |
| B | 17.70 | 2.85 | 1.23 | 0.79 | 0.45 | 0.35 | 0.40 |
| C | 16.51 | 2.56 | 0.67 | 0.26 | 0.30 | 0.20 | 0.14 |
| D | 14.66 | 2.69 | 0.28 | 0.84 | 0.30 | 0.23 | 0.23 |
| E | 12.45 | 2.25 | 0.36 | 0.24 | 0.21 | 0.09 | 0.03 |
| F | 15.23 | 2.65 | 0.71 | 0.46 | 0.30 | 0.16 | 0.17 |
| G | 20.21 | 5.02 | 2.16 | 1.54 | 0.23 | 0.29 | 0.24 |
| H | 23.98 | 1.23 | 0.57 | 0.36 | 0.24 | 0.02 | 0.01 |
| I | 15.20 | 2.77 | 0.85 | 0.30 | 0.15 | 0.19 | 0.11 |
| J | 21.06 | 1.42 | 1.96 | 0.14 | 0.20 | 0.12 | 0.07 |
| K | 31.97 | 9.13 | 3.58 | 1.68 | 1.31 | 0.68 | 0.76 |
| L | 18.49 | 0.95 | 0.57 | 0.26 | 0.23 | 0.13 | 0.09 |
| M | 24.32 | 6.20 | 1.90 | 0.26 | 0.05 | 0.25 | 0.04 |
| N | 30.24 | 3.07 | 1.26 | 0.56 | 0.36 | 0.18 | 0.19 |
| O | 39.36 | 4.04 | 2.85 | 3.58 | 2.37 | 0.00 | 0.87 |
| P | 8.40 | 3.16 | 1.19 | 0.17 | 0.10 | 0.10 | 0.17 |
| Q | 16.97 | 2.36 | 0.91 | 0.72 | 0.30 | 0.38 | 0.21 |
| R | 19.61 | 5.55 | 1.47 | 1.03 | 0.49 | 0.36 | 0.19 |
| S | 15.23 | 2.84 | 0.59 | 0.26 | 0.23 | 0.06 | 0.19 |
| S2 | 19.17 | 4.57 | 1.25 | 0.62 | 0.36 | 0.23 | 0.19 |
| T | 14.66 | 2.36 | 0.61 | 0.22 | 0.19 | 0.11 | 0.06 |
| *Percent area coverage from scanned water sensitive paper - 2.54 X 7.62 cm. **Product code is located in Appendix A. ***Heavier amounts due swath displacement in wind. |

Figure 3. LS Means for horizontal drift deposits recorded as percent area coverage on water sensitive paper for twenty-one products.

Figure 4. LS Means horizontal drift deposits on collectors at 50 – 350 feet downwind, recorded as percent area coverage on water sensitive paper for twenty-one products.  Scales are different to help separate differences.

Table 3. LS Means for vertical drift deposits recorded as gallons per acre on water sensitive paper for twenty-one products*.

|  | Feet |
| --- | --- |
| Product** | 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 |
| A | 0.03 | 0.12 | 0.10 | 0.05 | 0.02 | 0.07 | 0.13 | 0.11 | 0.03 |
| B | 0.11 | 0.21 | 0.21 | 0.19 | 0.16 | 0.23 | 0.13 | 0.09 | 0.08 |
| C | 0.07 | 0.25 | 0.28 | 0.26 | 0.19 | 0.15 | 0.17 | 0.16 | 0.14 |
| D | 0.06 | 0.14 | 0.09 | 0.08 | 0.04 | 0.05 | 0.04 | 0.08 | 0.06 |
| E | 0.01 | 0.03 | 0.01 | 0.02 | 0.04 | 0.10 | 0.04 | 0.04 | 0.04 |
| F | 0.01 | 0.02 | 0.00 | 0.00 | 0.04 | 0.06 | 0.02 | 0.08 | 0.07 |
| G | 0.07 | 0.18 | 0.21 | 0.23 | 0.24 | 0.24 | 0.18 | 0.19 | 0.17 |
| H | 0.02 | 0.00 | 0.01 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.01 |
| I | 0.04 | 0.10 | 0.10 | 0.08 | 0.08 | 0.09 | 0.09 | 0.08 | 0.07 |
| J | 0.02 | 0.08 | 0.12 | 0.11 | 0.10 | 0.10 | 0.08 | 0.09 | 0.08 |
| K | 0.18 | 1.24 | 2.25 | 1.30 | 1.14 | 0.76 | 0.84 | 0.46 | 0.37 |
| L | 0.00 | 0.01 | 0.03 | 0.04 | 0.03 | 0.05 | 0.03 | 0.02 | 0.00 |
| M | 0.07 | 0.11 | 0.29 | 0.27 | 0.18 | 0.18 | 0.00 | 0.03 | 0.00 |
| N | 0.06 | 0.15 | 0.15 | 0.16 | 0.14 | 0.11 | 0.12 | 0.10 | 0.09 |
| O | 0.02 | 0.26 | 0.18 | 0.00 | 0.06 | 0.29 | 0.07 | 0.01 | 0.29 |
| P | 0.09 | 0.31 | 0.51 | 0.33 | 0.30 | 0.22 | 0.25 | 0.17 | 0.18 |
| Q | 0.07 | 0.22 | 0.43 | 0.29 | 0.24 | 0.20 | 0.15 | 0.11 | 0.10 |
| R | 0.01 | 0.20 | 0.30 | 0.29 | 0.31 | 0.24 | 0.30 | 0.27 | 0.27 |
| S | 0.07 | 0.04 | 0.08 | 0.08 | 0.04 | 0.04 | 0.06 | 0.02 | 0.02 |
| S2 | 0.02 | 0.18 | 0.23 | 0.25 | 0.17 | 0.17 | 0.15 | 0.12 | 0.07 |
| T | 0.02 | 0.06 | 0.08 | 0.08 | 0.07 | 0.06 | 0.06 | 0.04 | 0.03 |
| *Gallons per acre from scanned water sensitive paper - 2.54 X 7.62 cm. **Product code is located in Appendix A. |

Figure 5. LS Means for vertical drift deposits recorded as gallons per acre on water sensitive paper for twenty-one products.

Table 4. LS Means for vertical drift deposits recorded as percent area coverage on water sensitive paper for twenty products*.

|  | feet |
| --- | --- |
| Product** | 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 |
| A | 0.10 | 0.39 | 0.29 | 0.19 | 0.18 | 0.29 | 0.24 | 0.40 | 0.15 |
| B | 0.37 | 0.78 | 0.80 | 0.73 | 0.61 | 0.78 | 0.47 | 0.34 | 0.29 |
| C | 0.26 | 0.80 | 0.91 | 0.84 | 0.64 | 0.50 | 0.53 | 0.54 | 0.47 |
| D | 0.20 | 0.61 | 0.46 | 0.39 | 0.25 | 0.21 | 0.23 | 0.28 | 0.20 |
| E | 0.04 | 0.12 | 0.08 | 0.12 | 0.16 | 0.34 | 0.18 | 0.18 | 0.15 |
| F | 0.01 | 0.14 | 0.04 | 0.01 | 0.19 | 0.25 | 0.13 | 0.27 | 0.26 |
| G | 0.23 | 0.60 | 0.73 | 0.75 | 0.78 | 0.81 | 0.61 | 0.63 | 0.56 |
| H | 0.02 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.03 |
| I | 0.13 | 0.33 | 0.34 | 0.28 | 0.30 | 0.31 | 0.31 | 0.28 | 0.24 |
| J | 0.23 | 0.31 | 0.40 | 0.38 | 0.33 | 0.35 | 0.27 | 0.28 | 0.27 |
| K | 0.65 | 3.28 | 4.99 | 3.71 | 3.24 | 2.21 | 2.28 | 1.28 | 1.00 |
| L | 0.01 | 0.07 | 0.14 | 0.15 | 0.11 | 0.18 | 0.11 | 0.05 | 0.00 |
| M | 0.34 | 0.43 | 0.93 | 0.93 | 0.75 | 0.71 | 0.08 | 0.23 | 0.00 |
| N | 0.22 | 0.51 | 0.55 | 0.58 | 0.50 | 0.42 | 0.44 | 0.38 | 0.34 |
| O | 0.26 | 1.00 | 0.96 | 0.00 | 0.32 | 0.74 | 0.51 | 0.24 | 1.01 |
| P | 0.16 | 1.01 | 1.46 | 1.05 | 0.98 | 0.70 | 0.80 | 0.60 | 0.58 |
| Q | 0.28 | 0.73 | 1.30 | 0.94 | 0.80 | 0.69 | 0.55 | 0.41 | 0.35 |
| R | 0.25 | 0.70 | 1.02 | 1.02 | 1.05 | 0.82 | 1.02 | 0.92 | 0.91 |
| S | 0.05 | 0.16 | 0.28 | 0.27 | 0.17 | 0.15 | 0.18 | 0.07 | 0.07 |
| S2 | 0.22 | 0.62 | 0.80 | 0.85 | 0.63 | 0.60 | 0.54 | 0.40 | 0.26 |
| T | 0.07 | 0.23 | 0.30 | 0.28 | 0.25 | 0.25 | 0.22 | 0.15 | 0.10 |
| *Percent area coverage from scanned water sensitive paper - 2.54 X 7.62 cm. **Product code is located in Appendix A. |

Figure 6. LS Means vertical drift deposits recorded as percent area coverage on water sensitive paper for twenty-one products.

# Text boxes

Preliminary Results

Preliminary Results

Preliminary Results

Preliminary Results

Preliminary Results

Preliminary Results

Preliminary Results

Preliminary Results